## Slide 1
MARDI_TECH · ONBOARD SENSOR STACK
OVERVIEW
Sensor Fusion & Bed Detection
Three ROS 2 services running on a Jetson Orin Nano turn a serial GNSS receiver, a BLE IMU, and a USB camera into a live, GPS-aware detection dashboard.
ROS 2 Humble
TensorRT
Docker Compose
Jetson Orin Nano
01 / 09

## Slide 2
THE CHAIN
Raw sensors to a live dashboard, in three services
SERVICE 01
sensor_data_raw
Serial GNSS receiver + BLE IMU. Publishes raw position fixes and orientation data onto ROS topics.
→
SERVICE 02
imu_gnss_raw
15-state error-state Kalman filter fuses GNSS + IMU into a smooth position, heading, and forward/backward motion state.
→
SERVICE 03
yolov8-trt-bed-detect-orin
TensorRT camera detection, gated and geotagged by the fused motion state. Serves the web dashboard.
All three talk only over ROS 2 topics on the loopback DDS domain — no direct API coupling between containers.
02 / 09

## Slide 3
SERVICE 01
sensor_data_raw — the raw feed
Two nodes bridge physical hardware onto ROS topics: a serial JSON reader for the GNSS receiver, and a BLE driver for the IMU.
▸
/gnss/pvt — std_msgs/String, raw PVT JSON
▸
/receiver/fix — sensor_msgs/NavSatFix
▸
/imu/data_raw → /imu/data — sensor_msgs/Imu, via complementary filter
The GNSS receiver is pinned to a fixed device path (/dev/gnss_rtk) via a udev rule keyed to its physical USB port — so USB enumeration order can never swap it silently.
03 / 09

## Slide 4
SERVICE 02
imu_gnss_raw — the fusion core
A single node, gnss_imu_eskf_node, runs a 15-state error-state Kalman filter — position, velocity, orientation, and both IMU biases.
15
Filter states tracked
~100Hz
IMU strapdown prediction rate
100
Stationary samples for bias init
3
Motion states: idle / forward / backward
Publishes both a fused estimate and a raw-GNSS-only estimate side by side — useful for validating the filter against ground truth in the field.
04 / 09

## Slide 5
SERVICE 03
yolov8-trt-bed-detect-orin — detection + dashboard
DETECTION NODE
WEB DASHBOARD
▸
TensorRT inference
YOLOv8 engine, GPU or CPU NMS, on-Jetson
▸
MOSSE tracking
Optional cumulative unique-object counting
▸
Started on demand
Not running by default — the dashboard starts it
▸
Live counts & MJPEG
Real-time view at :8090 and :8080
▸
GNSS-gated auto-save
Saves only while moving forward, past a distance threshold
▸
Model management
Upload, convert, and hot-swap engines live
05 / 09

## Slide 6
CLOSING THE LOOP
The dashboard talks back to the fusion node
The detection service doesn't just consume position data — it can retune the fusion filter live from the browser.
←
GNSS_FIX_TOPIC = /receiver/fix — dashboard lat/lon
←
MOTION_STATE_TOPIC = /gnss_imu_eskf/motion_state_raw_gnss — direction
←
GNSS_ONLY_ODOM_TOPIC = /gnss_imu_eskf/gnss_only_odom — auto-save distance gating
→
MOTION_POS_DEADBAND_TOPIC = /gnss_imu_eskf/motion_pos_deadband — dashboard writes back
06 / 09

## Slide 7
API SURFACE
32 endpoints across 7 groups
REST + WebSocket, covering live state, detection control, model lifecycle, saved-image management, and system power.
GET /api/status
POST /api/start
POST /api/stop
POST /api/auto_save
POST /api/motion_pos_deadband
GET /api/models
POST /api/models/build_engine
POST /api/deserialize/model
GET /api/report
GET /api/images/download
WS /ws
POST /api/shutdown
Full method / route / body reference lives in the API Reference document.
07 / 09

## Slide 8
WORTH KNOWING
Documented drift between code and docs
Research for this documentation surfaced a few real discrepancies worth resolving, not just typos.
Engine path swap risk
The aarch64-mounted config defaults to the x86 engine file path — worth confirming which engine actually loads on the Orin.
Undeclared filter params
Several tuning values in the ESKF's YAML aren't wired into the node's code and are silently ignored.
Stale IMU package README
Describes an older architecture with topic names that no longer match the deployed launch graph.
Hardware mismatch in README
Detection package prerequisites describe Jetson Nano; the actual build targets Jetson Orin Nano.
08 / 09

## Slide 9
READ NEXT
Full documentation set
This deck is the overview. For hands-on use and implementation detail, go to:
User Manual
Starting the system, dashboard walkthrough, troubleshooting
Developer Manual
Full topic/parameter tables, architecture, known drift
API Reference
Every HTTP + WebSocket endpoint, request/response shapes
09 / 09